## Slide 1: CBA Results Files Analysing the results

## Slide 2: Getting started
We highly encourage you to
  Read the CBA Methodology:
    Annex F on Methodology of TYNDP 2015
  http://www.entsog.eu/public/uploads/files/publications/TYNDP/2015/TYNDP022-150316_Annex_F_lowres.pdf
    And ESW-CBA Methodology
  http://www.entsog.eu/public/uploads/files/publications/CBA/2015/INV0175-150213_Adapted_ESW-CBA_Methodology.pdf
  Read the TYNDP 2015
  http://www.entsog.eu/publications/tyndp#ENTSOG-TEN-YEAR-NETWORK-DEVELOPMENT-PLAN-2015

## Slide 3: Usually expected impact
Capacity-based results
Result File | Indicator range in Initial/Final Situation | Group usually expected impact | Possible exceptions * (*) non exhaustive
IMPORT ROUTE DIV | [0 – 10 000] The lower, the better the diversification is | Decrease | Group increasing a country’s largest infrastructure capacity
N-1_ESW-CBA | [0% - no limit] The higher, the better the resilience is. | Increase | 

## Slide 4: Usually expected impact
Modelling results
Result File | Indicator range in Initial/Final Situation | Group usually expected impact | Possible exceptions * (*) non exhaustive
DISRUPTED RATE | [0% - 100%] The lower, the better | Decrease (eg -12%) | 
REMAINING FLEXIBILITY | [0% - 100%] The higher, the better the resilience is | Increase (eg +23%) | Group solving disruption
INDICATOR – USSD/CSSD | [0% - 100%] The lower, the lower the dependence is | Decrease (eg -8%) | Group solving disruption
INDICATOR – SSPDe | [0% - 100%] The lower, the lower the price exposure is | Decrease (eg -10%) | increase in a supply price curve Group solving disruption
INDICATOR – SSPDi | [0% - 100%] The higher, the better | Increase (eg +7%) | Group solving disruption

## Slide 5: Usually expected impact
Modelling results
Result File | Indicator range in Initial/Final Situation | Group usually expected impact | Possible exceptions * (*) non exhaustive
MONETIZATION (Total EU Bill) | The lower, the better | Decrease | Group allowing gazeification of new countries LNG terminals under LNG expensive, due to minimum send-out set on LNG terminals at 10% of send-out capacity LNG terminals causing increased 2W disruption in some price configurations

## Slide 6
celine.heidrecheid@entsog.eu; adam.balogh@entsog.eu