## Slide 1: TYNDP 2013-2022 SJWS #1 Infrastructure Projects -- Supply & Demand
TYNDP 2013-2022 -- 1st SJWS
24 January 2012
ENTSOG offices -- Brussels

## Slide 2: SJWS concept applied to TYNDP
Get a better understanding of stakeholders’ expectation
  Overall targets of TYNDP provided by Regulation
    Supply adequacy assessment
    Investment gap identification
    Identification of barriers to investments closing the gap
  Methodology needs to be enhanced according to stakeholders’ feedback in order to meet their expectations in the most appropriate way
Ensure access to knowledge beyond TSOs’ remit
  As TYNDP scope exceeds demand and transmission capacity direct input from other stakeholders are required to face TYNDP target
  Accuracy of the final report always reflects the lowest quality input, this implies that methodological improvements can be implemented only if the related data are provided to ENTSOG
<number>
Notes: <number>

## Slide 3: SJWS process
Build robust common understanding
  TYNDP is a thick report encompassing many topics making it difficult for non specialist to extract the entire added-value
  Continuous interaction with stakeholders during the process is key to ensure a good readability, involvement process thus needs to be further improved
  First part of the SJWS is to ensure a common understanding of previous report and received feedback
Analyze ENTSOG initial proposals
  Once common understanding will be reached, ENTSOG will release an initial proposal for each topic to be discussed with stakeholders
Final definition of methodology and inputs
  Based on the information and expectations coming from the SJWS, ENTSOG will define the methodology and data to be used in TYNDP 2013-2022
  Conclusions will be presented during June WS for final feedback prior to drafting process
<number>
Notes: <number>

## Slide 4: Infrastructure projects - General
TYNDP scope
  Current report covers:
    All types of infrastructures: transmission, LNG and UGS
    Both TSOs and third-parties’ projects (regulated or not)
  To be included, project information had to be submitted through a standard questionnaire (following a public call for information)
Public call rationale
  As project inclusion in TYNDP is a sensitive issue (that could increase with EIP), transparency and non-discrimination standards are of the highest importance
  Standard compliance are key when collecting data on a voluntary basis
Project clustering for modelling
<number>
  Regarding the wide range of projects included in TYNDP and the difference in investment process within Europe (see EIP discussion), FID is perceived by ENTSOG and many stakeholders as the most relevant, transparent and non-discriminatory criteria for clustering
Notes: <number>

## Slide 5: Infrastructure projects - What is in the TYNDP
Annex A
  Most comprehensive and detailed list of gas infrastructure projects across Europe
  Reference document built on project sponsors’ questionnaires
Main report: gap and remedy identification
  Under each of the 67 simulations, gaps have been identified if the country remaining flexibility was below 5% (or 1% in case of a disruption)
  If a project being part of Annex A mitigates the gap, it will be mentioned along with the gap (most of the time more than one project reduced the gap)
Annex E
  As either all FID or all FID plus non-FID projects have been clustered (including competing ones), the modeled load factor of projects in each scenario is lower than the one that could result having less projects coming on stream
  Nevertheless load factor of each individual project may be estimated using the remaining flexibility provided for projects in Annex E for most scenarios
<number>
Notes: <number>

## Slide 6: Submitted projects per category
<number>
Pipes | FID | Non-FID
Projects | 62 | 97
UGS | FID | Non-FID
Projects | 26 | 22
LNG | FID | Non-FID
Projects | 11 | 20
Total | FID | Non-FID
Projects | 99 | 139

## Slide 7: Infrastructure project questionnaire
<number>
Nearly the same questionnaire for TSOs’ and 3rd Parties’ projects

## Slide 8: Information provided within the report
<number>
Ukrainian disruption (additional investment gaps to the Reference Case) |  |  |  | 
BG | <1% | Reg. Cong. | Global improvement due to AT & SK > HU | <1%
HR | <1% | Reg. Cong. |  | <1%
FY | <1% | Reg. Cong. |  | <1%
GR | <1% | BG & TK > GR |  | <1%
HU | <1% | AT & SK > HU |  | <1%
RO | <1% | Reg. Cong. |  | <1%
RS | <1% | Reg. Cong. |  | <1%
Total High Daily demand for the region defined by all above countries is covered by 70% with existing infrastructure plus FID and by 75% with addition of non-FID projects. Individual country’s supply demand balance cannot be assessed in this TYNDP due to the current lack of criteria. With non-FID projects (AT to HU capacity increase) remaining flexibility for Austria is inferior to one per cent but still enable to cover the whole demand. |  |  |  | 
Numerical information within main body and non-FID project load factor within Annex E

## Slide 9: Infrastructure projects - Feedback
<number>
Data collection & processing
  Collecting process to be improved in order to ease submission by project sponsors
  Cost estimation should be provided on a voluntary basis
  Cost information should remain aggregated at report level
  Only the information needed for modelling purpose should be mandatory
  ENTSOG should have published detailed cost estimation as provided by project sponsors
  More promotion in order to have more projects committed
  Monitoring chapter on project progress should be added
  Explanation of differences between nTYNDP and GRIPs
  Interaction between TYNDP and PCI process should be explored
Project clustering
  FID is a relevant and objective criteria and any additional one should be easily verifiable
  Additional status could be “under construction” , “agreed but non-FID”
Existing infrastructures
  More detailed information should be provided

## Slide 10: Demand - General
TYNDP scope
  Current report covers:
    Demand scenario coming from TSOs (best estimates)
      An Average Daily Demand
      A High Daily Demand (1-in-20 in most countries)
    Annual demand scenarios coming from Eurogas, IEA and Primes
      An Average Daily Demand
  Only TSOs and Primes scenarios provide data on a country basis
Methodology rationales
  TSOs scenario has been factored in network modelling under both Average Daily Demand (proxy for yearly demand) and High Daily Demand
<number>
  As demand is used in modelling for gap identification, daily figures for each country were required
Notes: <number>

## Slide 11: Demand – What is in the TYNDP
Annex C
  Quantitative analysis and comparison of demand scenarios at European (and national level when possible)
Main report: overall supply adequacy to demand
  Comparison of TSOs demand scenario (yearly/average day picture) with potential supply at European level
  High Daily Demand comparison requires modelling as investment gaps could prevent available supply to move to demand centres
Resilience test
  Security of Supply resilience has been assessed under High Daily Demand as being the most stressful in case of disruption or low UGS deliverability
  Market integration resilience has been assessed under Average Daily Demand as competition is measured under business-as-usual conditions
<number>
Notes: <number>

## Slide 12: Demand - Feedback
<number>
Climatic criteria and alternatives
  Seasonal scenarios are more meaningful than yearly ones
  Additional top-down scenarios considering macro-economic indicators (population, GDP) the implementation of environmental and energy policy and alternative fuel mixes
  Impact of intermittent renewable power generation on gas demand
  Inclusion of third-countries as Norway and Turkey
  Higher transparency on the (individual) TSO’s underlying assumptions
  Consistent TSOs’ underlying assumptions
Comparative approach with other outlooks
  Coordination with ENTSO-E needs to be ensured
  Other outlooks could be also used in the modelled scenarios
  Analysis would have to be developed in order to check the consistency with renewable energy on a country-specific basis

## Slide 13: Supply - General
TYNDP scope
  Supply sources included in TYNDP were:
    Algeria (pipe) & Libya (pipe) from McDermott study for Commission
    LNG (all sources together) from a GLE study
    National Production from TSOs
    Norway and Russia from national Ministries
  Gathered information was potential supply on a yearly basis
Methodology rationales
  For each demand case (Average and High Daily) a supply case has to be defined to build a Reference Case
  In every resilience test scenario, supply has been kept as close as possible to the Reference Case while minimizing potential demand curtailment or investment gap and staying within the supply potential range of each source
<number>
  Supply mix in Reference Case is then used only to produce a reasonable scenario but has no influence on gap identification
Notes: <number>

## Slide 14: Supply – What is in the TYNDP
Annex C
  Comparison of yearly potential supply for every source
Supply under Average Daily Demand
  National production is set at maximum possible level
  2011 import shares are based on 2008 and 2009 average (BP Review)
  Starting in 2012, import shares are increased according to net demand (national demand less national production) until they reach their maximum potential
  In such case missing quantity is replaced by other sources
Supply under High Daily Demand
  National production is set at maximum possible level
  2011 import (except LNG) are based on 2008 and 2009 daily maximum flows
  Peak factor for 2011 has been defined for each import (except LNG) as the ratio between the share on the average day and the one of the High Daily Demand day
  Starting in 2012, such ratios have been applied for every source average share
  UGS and LNG have been used as last resort supply to balance the demand
<number>
Notes: <number>

## Slide 15: Supply - Feedback
<number>
General consideration on supply approach
  Consideration of supply limitation makes scenarios more realistic
  Ministerial sources could be too optimistic
  Non-conventional gas should be considered
  Dialogue with producers should be maintained and enhanced
  Consideration of ramp-up phases
  Focus should be on existing (contracted) supply and ones associated with committed projects
Supply modelling
  A 10 to 15-year average could be more relevant than 2008 & 2009 when defining supply shares for the Reference Case
  Methodology to define Reference Case supply is appropriate
  The arrival of a new supply source should reduce the shares of the existing ones
  Supply contractual constraints should be factored in the scenarios
  More supply scenarios should be investigated

## Slide 16: Average daily supply share – Reference Case
<number>
GWh/d |  | 2011 | 2015 | 2020
Demand |  | 1000 | 1200 | 1400
National Production | Potential | 300 | 250 | 200
 | Actual share | 300 | 250 | 200
Net Demand |  | 700 | 950 (+36%) | 1200 (+26%)
Supply A | Potential | 600 | 700 | 800
 | Actual share | 400 | 543 | 700 / 646
Supply B | Potential | 400 | 450 | 500
 | Actual share | 300 | 407 | 500 / 461
Supply C (hypothetic) | Potential | 0 | 0 | 0 / 100
 | Actual share | 0 | 0 | 0 / 93
Notes: <number>

## Slide 17: High daily supply share – Reference Case
<number>
GWh/d |  | 2011 | 2015 | 2020
Demand |  | 1400 | 1700 | 2000
National Production | Potential | 350 | 300 | 250
 | Actual share | 350 | 300 | 250
Net Demand |  | 1050 | 1400 | 1750
Supply A | Average Daily | 400 | 543 | 700
 | High Daily share | 500 | 679 | 875
Supply B | Average Daily | 300 | 407 | 500
 | High Daily share | 400 | 541 | 665
To be covered by UGS and LNG at same load factor |  | 150 | 180 | 210
GWh/d | Max 2008/2009 | Average daily share | High Daily Ratio
Supply A | 500 | 400 | 1.25
Supply B | 400 | 300 | 1.33
Notes: <number>

## Slide 18: Supply by import route
<number>
Load factor of import routes coming from other supply sources are not impacted by the new Route 3

## Slide 19: Thank You for Your Attention
<number>
ENTSOG -- European Network of Transmission System Operators for Gas
Avenue de Cortenbergh 100, B-1000 Brussels
EML: info@entsog.eu
T: + 32 2 894 5100
WWW: www.entsog.eu