## Slide 1: Network & market modelling ENTSOG tool handbook

## Slide 2: Why ENTSOG needs a modelling tool ?
ENTSOG has inherited the GIE expert role within the GCG
  Modelling of the whole gas infrastructure (Transmission, UGS and LNG)
  Regular presentation of ENTSOG reports (Outlooks and TYNDP)
  Ad hoc study asked by COM (mostly disruption scenarios)
ENTSOG obligations under the 3rd Energy Package
  Supply adequacy and investment gap identification as carried out within TYNDP and Supply outlooks require a tool checking the ability to transport gas from supply to consumption areas
  Such tool needs to be consistent with the concept defined by the Regulation: Entry/Exit zones, hub-to-hub products and firm capacity
Future expectations coming from Connecting Europe Facility
  CBA methodology to be developed by ENTSOG should be based on a gas Network and Market model
  Possible extension to a common model for electricity and gas by 2016
<number>
Notes: <number>

## Slide 3: Philosophy of ENTSOG model
European top-down approach
  ENTSOG’s focus is on European and cross-border issues
  Only a top-down approach may identify the influence of one system behaviour on the adjacent ones
Network modelling based on the capacity sale model
  Modelling tool has to be consistent with adjacent Entry/Exit zones linked by cross-border capacity as targeted by the 3rd Energy Package
  Network resilience assessment has then to be consistent with the market structure
  Market should manage all situations including crisis as far as infrastructure are available
Embedded hydraulic simulation
  Results from TSOs hydraulic capacity calculation are factored in ENTSOG modelling tool through firm capacity
  No additional need to consider hydraulic simulation at the European level.
<number>
Notes: <number>

## Slide 4: Overview of the European gas system
<number>
Notes: <number>

## Slide 5: Model inputs
Demand
  A demand figure is attached to every node of the system standing for an entry/exit zone
Supply
  For each supply source are considered:
    The potential supply toward Europe
    The import capacity per route
    A control range standing for upstream constraint or historical range of flows
    A weight in order to define priority between supply sources
Capacity
  Hub-to-hub capacity is derived from the firm capacity as calculated by TSOs on both sides of every IP between two entry/exit zone
<number>
Notes: <number>

## Slide 6: Model topology
<number>
Notes: <number>

## Slide 7: European gas system topology used by the tool
<number>
Notes: <number>

## Slide 8: Tool functioning
Basic functioning
  Find a flow pattern meeting the following constraints:
    Arcs: flows are within the lower/upper range defined for each arc
    Nodes: flow pattern balances every node
Multiple time units period
  Basic period is one day and multiple day periods such as month or seasons may modelled as one average day or consecutive individual days
  In latter case, UGS and LNG stock level are updated between 2 simulations
System resilience determination
  Investigation of the limits of the European gas system
  Use of optimization using an objective function describing he direction to be investigated
<number>
Notes: <number>

## Slide 9: Overall modelling process
<number>

## Slide 10: UGS and LNG tank level consideration
Capacity vs. Volume assessment
  TSOs’ task and main ENTSOG commitment is related to the resilience of the transmission network. Is capacity sufficient to face the most challenging day?
  Supply adequacy checking is also an ENTSOG task and encompasses a temporal (or volume dimension) through supply availability on a given period but cannot be carried out without stakeholders involvement as being beyond the scope of TSOs activities
Volume consideration
  Stakeholders assessment is key to assess supply availability
  Storage (UGS and LNG tank) infrastructure modeling is made possible through close collaboration with GSE and GLE:
    UGS stock level vs. deliverability curve
    LNG tank management and ship unloading
<number>
Notes: <number>

## Slide 11: Embedded optimization engine
<number>
Notes: <number>