## Slide 1: Market Integration & SoS Initial proposals for SJWS #5
ENTSOG offices – Brussels
Stakeholder Joint Working Session – 20 March 2012

## Slide 2: SJWS process on SoS & Market Integration
<number>
February session – Come-back to TYNDP 2011-2020
  Establishment of a shared understanding of current report and associated feedback
March session – ENTSOG initial proposals
  Proposals focus on selection of relevant cases for SoS & Mkt Int. assessment
  Feedback on proposals and first considerations on indicators to be used
April session – ENTSOG updated proposals
  Fine-tuned scenarios and first set of indicators
May session – Fine-tuning of assessment methodology
  Presentation of an integrated method (cases & indicators) fitting with other SJWSs
June TYNDP 2013-2022 Public WS
Feb. 15th
Mar.
20th
April
?
May
?
Notes: <number>

## Slide 3: Security of Supply
<number>
What should be considered when selecting Cases
  Main driver is the identification of potential investment gaps under realistic cases
  Modelling tool is no more a limitation but result analysis remains the key step
  Comparability with previous TYNDP in order to measure improvement /decline in the European gas system resilience
List of parameters defining as Case
  Demand scenario: ENTSOG (TSOs), NREAs, Primes…
  Infrastructure scenario: FID, non-FID
  Demand case: combination of period (1, 7 & 30 days) and methodology (Design, 1-in-20 & 1-in-2)
  Supply case: consistent with Demand case
  Potential events: none (Reference Case), technical disruption (NO, AL & LY), transit disruption (UA & BY) and supply disruption (Qatari LNG), low UGS deliverability
Notes: <number>

## Slide 4: Security of Supply – Demand Cases
<number>
Maximum transported energy
  This is a natural case to test the resilience of the European transmission system
  In this case demand is at the highest daily level and supply is assumed to be at its highest availability
  Level of demand can be defined in 2 ways:
    Design Case: in every country demand is set at the level defined as the reference for national design according national legislation (highest stress)
    » Ensure consistence between national and European plans
    1-in-20 Case(Diversified or not): demand is set in every country according a given occurrence
    » Ensure consistent risk across borders
Rationales of X-day cases
  Duration of an event impact in a different way demand level and each supply source
  These dissimilarities induce different transmission needs depending on the duration
  Stress on gas infrastructure is measured on one day (the last one is assumed to be the most stressful)
Notes: <number>

## Slide 5: Security of Supply – X-day cases
<number>
Definition of demand level on a X-day period
  Demand is assumed to be flat on the period
  Daily values from historical database used to define demand level are averaged on a X-day moving basis
Way to model
Modeled day
  Supply/Demand balance on the last day defines the need of UGS
  Modeling check potential gaps
  Ex-post calculation defines the minimum UGS level prior the case
Notes: <number>

## Slide 6: Security of Supply – potential events
<number>
Disruption events in current TYNDP, are they up to date?
  Ukraine and Belarus: total disruption of either transit
  Libya: total disruption of import pipe
  Algeria: 50% disruption of import pipes
  Norway: total disruption of Langeled pipeline
  LNG: Qatari disruption
  Value of a low UGS deliverability Case
  If the understanding of disruptions is quite straight forward, stakeholders’ expectations in term of impact of a low UGS deliverability is less clear
  Expected outputs
  Potential investment gaps
  Flexibility of the gas system at Entry/Exit zone level
Notes: <number>

## Slide 7: Security of Supply – Low UGS
<number>
Initial proposal
  In comparison with Reference Case, UGS deliverability is reduced by 10% then 20%
  Missing gas is caught up by imports still limited by their Potential Supply level
  Potential evolution
  UGS withdrawal rate at European level is defined by putting all imports at their Potential Supply level
  Case is then modeled either using:
    Same UGS withdrawal rate across Europe
    UGS withdrawal rate in each system set in order to minimize investment gaps
75%
75%
75%
75%
75%
75%
75%
80%
70%
75%
95%
80%
80%
60%
Or
Notes: <number>

## Slide 8: Security of Supply – Event management
<number>
Management of disruption or low UGS deliverability cases
  Supply priority is:
    Disrupted supply through alternative routes
    Alternative imports (including LNG until maximum potential supply)
    LNG (using remaining capacity up to 80% send-out load factor) and UGS
    Disruption
  Order does not influence the identification of gaps but provide transparency on the method and influence the resulting supply mix
Load factor of import routes
  Model will be able to use different load factor for routes between a given supply source and Europe
  Nevertheless a minimum load factor (derived from historical data) will be defined for every route
Notes: <number>

## Slide 9: Security of Supply
<number>
What should be considered when selecting Cases
  Main driver is the identification of potential limitation in the supply spread (not gap as potential benefit should be assessed against cost by the market )
  In which way infrastructures can support market integration (but not ensure it as it primarily depend on their use)
  Modelling tool is no more a limitation but result analysis remains the key step
  Comparability with previous TYNDP in order to measure improvement /decline in the European gas system resilience
List of parameters defining as Case
  Demand scenario: ENTSOG (TSOs), NREAs, Primes…
  Infrastructure scenario: FID, non-FID
  Demand case: average yearly day or seasonal values
  Supply case: consistent with Demand case
  Potential events: maximization/minimization of a set of supply sources
Notes: <number>

## Slide 10: Market Integration – Mini/Maximization
<number>
Supply mini/maximization
  Supply maximization helps to measure the potential physical reach of a supply source (same as current TYNDP)
  Supply minimization helps to measure the required minimum of a given source of gas in order to balance Europe (same as Winter Supply Outlook 2011/12 and providing some Security of Supply indication)
Level of stress
  Results (limitations, maximum reach and minimum supply) will highly depend on the level of stress defined by the following parameters:
Parameters | Combination of supplies | Upper supply limit | Lower supply limit
Options | One-by-one | 0 | Capacity
 | Per region | Derived from historical values | Maximum potential supply
 |  | Provided by stakeholders | 
Notes: <number>

## Slide 11: Market Integration – Combination of supplies
<number>
One-by-one (previous TYNDP) Per region
AL, LY & LNG
RU, AL, LY, CA, LNG -3%
RU, LNG & CA
NO +20%
NO, RU, LNG
  Regional approach may induce larger gas movement but may be less realistic with a given supply source moving in opposite direction depending the considered region
Notes: <number>

## Slide 12: Market Integration – Demand Cases
<number>
Demand cases
  Demand levels have a direct influence on the assessment results:
    They define the considered period (a year or a season)
    Higher demand is more stressful in case of supply minimization (Winter)
    Lower demand is more stressful in case of supply maximization (Lower)
Role of the UGS
  In current TYNDP, the UGS has been kept neutral (no withdrawal or injection) which:
    Avoids to make assumption on their use
    Disregards their impact on the maxi/minimization
Notes: <number>

## Slide 13: Security of Supply & Market Integration proposed Cases
<number>
List of parameters
  Initial proposal accounts for 200 cases (against 67 for TYNDP 2011-2020), list will be updated considering your feedback
Year | Infra. Cluster | Demand Case Duration Occurence |  | Disruption | UGS deliverability | Supply source mix
2012 | FID | 1 day | Peak 1 | None | No use | Reference
2017 | Non-FID | 7 days | Peak 2 | AL | Not limited | Crisis
2022 |  | 30 days | Average Winter | LY | -10% / Ref Case | Min/max AL
 |  | Year | Average | BY | -20% / Ref Case | Min/max LY
 |  |  |  | UA |  | Min/max BY
 |  |  |  | NO |  | Min/max UA
 |  |  |  | LNG |  | Min/max NO
 |  |  |  |  |  | Min/max LNG
Notes: <number>

## Slide 14: Thank You for Your Attention
<number>
Olivier Lebois, Adviser, System Development
ENTSOG -- European Network of Transmission System Operators for Gas
Avenue de Cortenbergh 100, B-1000 Brussels
EML: Olivier.Lebois@entsog.eu
T: + 32 2 894 5105
WWW: www.entsog.eu