## Slide 1: TYNDP 2013-2022 concept SJWS #7 – conclusion on TYNDP concept
TYNDP 2013-2022 Stakeholder Joint Working Session – 29 May 2012

## Slide 2: TYNDP concept
<number>
Assessment of the European gas infrastructure system
  Being a network development plan, TYNDP focuses on infrastructures
  Supply adequacy outlook has to be checked at aggregated European level and at local one (balancing zone) as demand and supply levels and locations have a direct influence on the need of infrastructures
  Considered scenarios/cases have to be stressful but still realistic
  Top-down layer enabling the identification of trends and impacts that cannot be identified at national level because of a very meshed European network
  Results consist in:
    Indicators assessing SoS, Market Integration…
    Identification of investment gaps hampering demand cover
ENTSOG TYNDP is not
  A forecast
  An assessment of the good implementation of market rules
  A strategic study of producing/transit countries
Notes: <number>

## Slide 3: Process timeline
<number>
From concept to reality
  Concept derived from previous TYNDP consultation, ACER’s opinion and SJWSs
  It will be presented and explained during June WS to facilitate future understanding
  Data collection and report drafting can then start based on a mature concept
Notes: <number>

## Slide 4: Report structure
<number>
Aggregated supply adequacy outlook
  Demand scenarios
  Supply scenarios
European gas infrastructure
  Overview of current system
  Infrastructure scenarios translated into mixed network-market topology
Infrastructure assessment
  Definition of cases and methodologies
  Investment gap identification
  Indicators assessing level of SoS and Market Integration
Annexes
  Detailed country and project profiles
  Input and output data from the assessment
Notes: <number>

## Slide 5: European gas infrastructure
<number>

## Slide 6: Overview of current situation
Basis for better understanding of future investment use/need
  Ease the comparison for the feeling of missing infrastructure under current market conditions and under an optimized use of infrastructures
  Provide background to infrastructure projects
Similar information than the ones provided by Syst. Dev. map
  Reference 2009, 2010 & 2011
  Information at aggregated cross-border level
  Information provided on seasonal or yearly basis:
    Average flow
    Maximum flow
<number>

## Slide 7: Network-market topology
DEn
NP
UGS
LNG
NO
BEx
UKx
IEx
NLx
LUx
DEg
FRn
FRs
FRt
ESx
PTx
CHx
ITx
DKx
SEx
ATx
SIx
CZx
PLg
HRx
HUx
RSx
SKx
PLy
ROx
ROt
BGx
FYx
GRx
UA
BY
LTx
EEx
FIx
KL
RU
LVx
TK
AL
LY
UGS, LNG & NP nodes, control nodes and arcs to all E/E systems
Actual topology depends on the year and infrastructure scenario
Notes: <number>

## Slide 8: UGS and LNG terminal modelling
LNG dual role
  LNG terminal send-out should consider the dual role of the facilities:
    The imports
    The storage
  LNG tank management (including stock level prior to the event) has to be defined for the 2-week case
  These elements are to be discussed with GLE
UGS curve
  Last Summer and Winter Supply Outlooks use a single and conservative deliverability curve (linked to stock level) for every country
  Potential improvement has to be considered with GSE
<number>

## Slide 9: Scenarios & Cases
<number>

## Slide 10: Scenario vs. Case
<number>
2 kind of scenarios
  Follow the evolution of one variable during the time
  Pathways: e.g. Roadmaps
  Forecast: e.g. best estimate
2012 2022 2050
Demand
Peaks 2-week peak Average
2017 cases
Cases are derived from scenario
  Average day
  2-week peak
  Daily peaks
Scenario comparison
Notes: <number>

## Slide 11: Considered scenarios and cases
<number>
Considered scenarios
  Demand scenarios: TSO, Primes, Eurogas
  Supply scenarios: Minimum, medium and maximum
  Infrastructure scenarios: Existing infra. + FID & Existing infra. + FID + non-FID
Different parameter setting when defining cases
Demand | Supply | Events
Design Case | Reference | BY disruption
Simultaneous peak | Predominant | UA disruption
2-week simultaneous peak | Minimum | NO disruption (specific infra. to be defined)
Yearly average |  | AL1 (through Tunisia)
 |  | AL2 (through Morocco)
 |  | LNG (update of GLE study)
Notes: <number>

## Slide 12: Supply potential
<number>
  Definition of a maximum, medium and minimum supply potential by source based on publicly available data from governmental and other sources.
  These levels are defined at yearly level. For the analysis they have been translated in the daily averages.
Upper limit: Test of Market Integration
Upper limit flexibility

## Slide 13: Matrix of cases - Reference
<number>
Notes: <number>

## Slide 14: Matrix of cases - SoS
<number>
Notes: <number>

## Slide 15: Matrix of cases – Market Integration
<number>
198 cases to compare to the 67 of TYNDP 2011-2020
Notes: <number>

## Slide 16: Infrastructure assessment
<number>

## Slide 17: Applied methodologies per case
<number>
Reference and disruption cases
  Calculation of Remaining Flexibility per entry/exit zone
  Investment gap and remedy identification
Minimum UGS deliverability cases
  Calculation of Remaining Flexibility per entry/exit zone
  Identification of systems where withdraw rates should be higher
  Calculation of required withdraw rates (stock levels) to face the event
Market integration
  Supply maximization: even reach and multiple maximum reach
    Identification of infrastructure preventing to reach a given supply share in every country (if any limitation)
  Supply minimization: even reduction
    Identification of infrastructure preventing (if any limitation) to reach the lower limit
  Supply/Route diversification index defined by country for both maximum and even reach
Notes: <number>

## Slide 18: Remaining flexibility & investment gaps
Remaining flexibility indicator
  It is defined at 2 levels:
    Infrastructure:
    System level:
  Results are provided as ranges: <1% / 1-5% / 5-20% / >20%
Gap identification criteria
  Under Reference Case (no disruption), gaps are identified when a system has a Rem. Flex below 5%
  In case of disruption, the criteria is decreased to 1% as part of the Rem. Flex will have been used to face the event
  Then congested infrastructure (or supply) are identified based on their Rem. Flex
  Potential remedies will be identified using the non-FID projects provided by project promoters (without priority)
<number>
Dependence to flow pattern
High
Medium

## Slide 19: Gap and remedy identification
<number>
 | FID case |  |  | Non-FID Case |  | 
Country | Rem. Flex | Curtailed demand | Congestion | Remedy | Rem. Flex | Curtailed demand
CC1 | 1-5% |  | Tra.: UGS: LNG: | Tra.: UGS: LNG: | 5-10% | 
CC2 | <1% | 20 GWh/d | Tra.: UGS: LNG: | Tra.: UGS: LNG: | <1% | 10 GWh/d
CC3 | <1% | 50 GWh/d | Tra.: UGS: LNG: | Tra.: UGS: LNG: | 1-5% | 
CC4 |  |  | Tra.: UGS: LNG: | Tra.: UGS: LNG: | <1% | 50 GWh/d
CC5 |  |  | Tra.: UGS: LNG: | Tra.: UGS: LNG: |  | 
Remedies will be identified if within the list of submitted infrastructure projects.
Specific reference will be made to the project to ease the reading

## Slide 20: Indicators (still to be discussed with stakeholders)
<number>

## Slide 21: Supply diversification
<number>
Impacting supply share
  The share of a given supply source able to induce a significant impact on prices
  Should it be calculated in comparison with the total supply or the total imports ?
  TYNDP 2011-2020 used mostly 5% (identifying also systems with more than 20%)
  On map, supply shares should be represented with figures or ranges?
Supply diversification from a market perspective
  Could be based on the uniform or maximum spreads
  Which is the minimum share of a given source to be considered?
  How to deal with LNG embedded diversification (e.g. highlighting the presence of LNG)?
  Is a benchmark (e.g. 3 sources required)?
Notes: <number>

## Slide 22: Route diversification
<number>
ENtry Capacity Concentration index
  Based on the same logic than HHI but calculated on the share of an entry capacity in the total entry
  A supply diversification index may be defined the same way using the flows coming from supply sources but index will then depend on flow pattern (which could be mitigated through a sensitivity study)
EXit Capacity Concentration index
  Similar indicators may defined based on exit capacity in order to measure how a system may support supply/route diversification
  Result should be compared to the idealistic situation taking into account the number of cross-borders
100%
40%
30%
20%
10%
ENCC=
100²= 10 000
ENCC=
40²+30²+20²+10²= 3000
As for all indicators, analysis is more robust when comparing situation of one country between 2 cases
Notes: <number>

## Slide 23: Range of infrastructure use in the cases
Synthetic indicator can be derived from all simulations
  Indicator can be defined for every system:
    At cross-border level
    UGS aggregate
    LNG aggregate
  Range would be defined base on the highest and lowest load factor of the 198 simulations (not considering Reference Cases)
<number>
  Actual use may be outside these ranges
  Robustness could be improved with a sensitivity study around each simulation modifying slightly the supply shares

## Slide 24
Supply
Definition of the reference case
<number>

## Slide 25: New approach: a more realistic reference cases
<number>
  Definition of Potential levels of Supply
  Daily average
  Supply shares by source:
    Average 2009-2010-2011 on the ENTSOG historical data base.
  Supply shares by route:
    The import flows by route are proportional to the historical utilization of the routes – average 2009-2010-2011.
  Peak Day
  A certain share of LNG is treated as pipeline gas -> Daily minimum LNG import. The remaining LNG import capacity, as well as the UGS are used as last resource sources, with common load factors.
  The pipeline imports are defined by the historical daily maximums by source (or by route).
Notes: <number>

## Slide 26
Definition of the reference case
AVERAGE DAY
<number>

## Slide 27: Average daily supply share – Reference Case
<number>
 |  |  |  | Iteration 0 | Iteration 1
GWh/d |  | 2011 | 2015 | 2020 | 2020
Demand |  | 1000 | 1200 | 1400 | 1400
National Production | Potential | 300 | 250 | 200 | 200
 | Actual share | 300 | 250 | 200 | 200
Net Demand |  | 700 | 950 | 1200 | 1200
Supply A | Potential | 600 | 700 | 800 | 800
 | Actual share | 400 (57%) | 543 (57%) | 687 (57%) | 700 (58%)
Supply B | Potential | 400 | 450 | 500 | 500
 | Actual share | 300 (43%) | 407 (43%) | 513 (43%) | 500 (42%)
Supply balance |  | 0 | 0 | 0 | 0
Notes: <number>

## Slide 28: New approach: a more realistic reference cases
<number>
  Definition of Potential levels of Supply
  Daily average
  Supply shares by source:
    Average 2009-2010-2011 on the ENTSOG historical data base.
  Supply shares by route:
    The import flows by route are proportional to the historical utilization of the routes – average 2009-2010-2011.
  Peak Day
  A certain share of LNG is treated as pipeline gas -> Daily minimum LNG import. The remaining LNG import capacity, as well as the UGS are used as last resource sources, with common load factors.
  The pipeline imports are defined by the historical daily maximums by source (or by route).
Notes: <number>

## Slide 29: Daily Average: Supply shares by Source
<number>
  Starting point: Average 2009-2010-2011
    Libyan exception: Avoid the effect of Libyan disruption, it’s contribution to the supply share measured by the average 2009-2010
  Small changes in the supply shares by source:
    Lower share:
      Norway
      Algeria
    Higher share:
      LNG
Notes: <number>

## Slide 30: Daily Average: Supply shares by Source
<number>
  Supply potential level by source: Medium supply potential
Dark colours: Average shares 2008-2009
Light colours: Average shares 2009-2010-2011
Notes: <number>

## Slide 31: Supply shares by route
<number>
Source 1
R1
R2
TYNDP 2011-2020 – Common route share
Source 1 – Balance: 600 Units
Route 1 – Technical capacity: 300 Units
Route 2 – Technical capacity: 300 Units
Route 3 – Technical capacity: 400 Units
Total technical capacity: 1000 Units: Load-factor: 60%
Route 1 – 180 Units
Route 2 – 180 Units
Route 3 - 240 Units
Historical load-factor of the routes (last 3 years)
Route 1 – 50% - 150 Units
Route 2 – 70% - 210 Units
Route 3 – 40% - 160 Units
Total: 520 Units
Different route share according to the historical data:
Route 1 = 600 * (150/520) = 173 Units
Route 2 = 600 * (210/520) = 242 Units
Route 3 = 600 * (160/520) = 184 Units
R3
Notes: <number>

## Slide 32: Supply shares by route. Results’ test
<number>
  Russian Routes
  The big differences between the historical load factors of the different routes lead to a significant change in the import shares by route when substituting the average load factor by a historical-based route shares.
  Due to the lack of historical data, an average load factor is used for Nordstream.
Notes: <number>

## Slide 33: Different approaches: Results test
<number>
  The average historical load factor of the Ukraine to Slovakia route (62%) is significantly over the Russian average (50%), therefore the utilization of this route would be significantly lower when considering an homogeneous value.
  The same is happening for the Belarus to Poland route (including Yamal), where the average historical load factor is 67%.
Notes: <number>

## Slide 34: Different approaches: Results test
<number>
  Due to the low average historical load factor of the route from Ukraine to Romania (7%) the utilization of an homogeneous load factor values would lead to too high import flows through this route .
  Something similar is found for the route from Ukraine to Hungary where the average historical load factor is 33%.
Notes: <number>

## Slide 35
Definition of the reference case
PEAK DAY
<number>

## Slide 36: High daily supply share – Reference Case
<number>
GWh/d |  | 2011 | 2015 | 2020
Demand |  | 1400 | 1700 | 2000
National Production | Potential | 350 | 300 | 250
 | Actual share | 350 | 300 | 250
Net Demand |  | 1050 | 1400 | 1750
Supply A | Average Daily | 400 | 543 | 700
 | High Daily share | 500 | 679 | 875
Supply B | Average Daily | 300 | 407 | 500
 | High Daily share | 400 | 541 | 665
To be covered by UGS and LNG at same load factor |  | 150 | 180 | 210
GWh/d | Max 2008/2009 | Average daily share | High Daily Ratio
Supply A | 500 | 400 | 1.25
Supply B | 400 | 300 | 1.33
Notes: <number>

## Slide 37: Proposed changes/improvements
<number>
Source 1
R1
R2
Maximum Historical supply from Source1: 13,000 Units – specific date
Route 1: 7,500 Units
Route 2: 5,500 Units
Maximum non-simultaneous supply from Source 1: 14,000 Units
Route 1: 8,000 Units
Route 2: 6,000 Units
Historical yearly supply from Source 1: 3,650,000 Units – Average 10,000 units
Peak supply from source 1:
TYNDP 2011-2020
Maximum non-simultaneous supply
Peak factor: Maximum/Average
14,000/10,000 ~ 1,4
Apply the historical peak factor to the “estimated” volumes in the future
This approach has been said to be to optimistic as the maximum flexibility may have been reached.
ALTERNATIVES
Maximum historical daily values without yearly volumes considerations:
  Maximum simultaneous supply (13,000)
  Maximum non-simultaneous supply (14,000)
Volume consideration - Peak factors:
  From the maximum simultaneous supply ~ 1,3
  From the maximum non simultaneous supply ~ 1,4
(*)
(*) Follow the TYNDP 2011-2020 methodology
Notes: <number>

## Slide 38: New approach: a more realistic reference cases
<number>
  Definition of Potential levels of Supply
  Daily average
  Supply shares by source:
    Average 2009-2010-2011 on the ENTSOG historical data base.
  Supply shares by route:
    The import flows by route are proportional to the historical utilization of the routes – average 2009-2010-2011.
  Peak Day
  A certain share of LNG is treated as pipeline gas -> Daily minimum LNG import. The remaining LNG import capacity, as well as the UGS are used as last resource sources, with common load factors.
  The pipeline imports are defined by the historical daily maximums by source (or by route).
Notes: <number>

## Slide 39: Different approaches: Results test
<number>
  Daily peak
Maximum historical daily values without yearly volumes considerations:
  Maximum simultaneous supply -> OPTION A
  Maximum non-simultaneous supply -> OPTION B
Volume consideration - Peak factors:
  From the maximum simultaneous supply -> OPTION C
  From the maximum non simultaneous supply -> OPTION D (TYNDP 2011-2020)
Notes: <number>

## Slide 40: Different approaches: Results test
<number>
Notes: <number>

## Slide 41: Different approaches: Results test
<number>
Notes: <number>

## Slide 42: Thank You for Your Attention
<number>
Olivier Lebois & Carmen Rodriguez, Advisers, System Development
ENTSOG -- European Network of Transmission System Operators for Gas
Avenue de Cortenbergh 100, B-1000 Brussels
EML: Olivier.Lebois@entsog.eu
Carmen.Rodriguez@entsog.eu
T: + 32 2 894 5105 / 5125
WWW: www.entsog.eu